## Slide 1: Vehicle Towing Requirements
All Allison transmissions must never be towed with the vehicle driveshaft(s) connected
  Except for the 3700SP
If driveshaft(s) are not removed prior to towing:
  Vehicle drive axles will rotate transmission output shaft at high speeds
    Output shaft becomes input shaft of transmission
    All gears, bearings, bushings and clutches rotate at high speed without lubrication
    Serious damage occurs
      Many times transmission is completely destroyed beyond economical repair
Vehicle may only be moved minimum distance with driveshaft(s) installed
  To a location that does not interfere with traffic so driveshaft(s) can be disconnected

## Slide 2: Vehicle Towing Requirements
Model 3700SP transmission
  Only transmission capable of being towed without removal of driveshaft(s)
  Equipped with integral transfer case
    Contains unique lubrication pump
      Provides lubrication to entire transmission
      Pump driven by transfer case gears
      Transfer case gears driven by vehicle driveshaft(s)
      Pump draws fluid from bottom of transfer case during towing

## Slide 3
Case Study
Issue
  Leasing company service manager stated truck stopped moving
  Driver pulled to side of road
  Smoke coming from under truck
  Truck in use as rental at time of failure.
    Vehicle mileage at failure 149,365 (240,380 Km)
Transmission
  3000 Series
Vocation
  Straight truck with box body (lease vehicle)

## Slide 4
Case Study
Component damage found:
Output Speed Sensor
P3 Planetary & Main Shaft Welded Together

## Slide 5
Case Study
Component damage found:
P2 Planetary Carrier Before Removal From P3 Ring Gear
Inside Rear of Main Case

## Slide 6
Case Study
Component damage found:
Internal Wiring Harness and Solenoid Connectors

## Slide 7
Case Study
At what temperatures would the output speed sensor and internal wiring harness connectors begin to melt?
  Output speed sensor made from 33% glass filled polamide
    Melting temperature 530-580 F (277-304 C)
  Internal wiring harness channel composed of heat stabilized Nylon 66
    Melting temperature 489-505 F (254-263 C)
  Not all transmission series use exact same materials, but melting points would be similar

## Slide 8
Case Study
Can a transmission operate with fluid at these temperatures?
  This transmission was filled with Transynd fluid
    TranSynd flash point is 455 F (235 C)
      Flash point is lowest temperature where vapor formed above a pool of liquid will ignite at a pressure of 1 atmosphere

## Slide 9
Case Study
Is it logical that an output speed sensor with a melting point of 530-580 F (277-304 C) would have melted from heat generated inside the transmission during operation?
  The answer is No.
    It is not possible for the transmission to continue operation until internal temperatures reached this point.
    Transmission fluid viscosity would have greatly increased at approx. 400 F (204 C)
      Would have become almost a paste at 500 F (260 C)

## Slide 10
Case Study
Would the charging pump continue to draw sufficient volume of fluid for proper transmission operation above 400 F (204 C)?
  The answer is also No
    Inspection of suction filter reveals very little debris captured on outside of filter
    Large amount of metal and aluminum particles found inside transmission (refer to image of rear main case)
    Suction filter would be full of debris if transmission was operating at time of failure
    Lack of debris in suction filter proves transmission was not operating via engine at time of failure

## Slide 11
Case Study
Typical suction filter debris level when transmission is functional during failure
Suction filter in Case Study transmission

## Slide 12
Case Study
Conclusion
  Epicenter of heat source was P3 planetary
    Clearly seen by heat discoloration of steel components
    Severity of melted internal wiring harness connectors and solenoids closest to P3 planetary
Air Aging Color Chart – 1 Hour of Exposure
All sections aged in same air-circulating oven for 1 hour at defined temperatures

## Slide 13
Case Study
Conclusion (cont’d)
  It is physically impossible for a transmission to operate under engine power and create extent of damage shown in P3 planetary gear set
  Damage due to insufficient/no lubrication under engine power does not manifest into this level of damage
  It is impossible to reach melting point of output speed sensor and wiring harness if transmission was being operated under engine power

## Slide 14
Case Study
Conclusion (cont’d)
  “I was driving the vehicle when it just stopped moving.”
    Common statement from vehicle driver and/or owner of a vehicle exhibiting damage caused by towing
    To disprove statement, inspect:
      Suction filter
      Charging pump gears
      Charging pump bushing

## Slide 15
Case Study
Conclusion (cont’d)
  Due to large amount of metallic debris found inside case study transmission:
    Debris would be present in suction filter if transmission was operational at time of failure
    Cleanliness of suction filter screen indicates this was not the case

## Slide 16
Case Study
Conclusion (cont’d)
  Further evidence engine was not operational:
    Scratches not present on tips of charging pump drive gear
    Radial scratches not present on bushing surface
    Indicates components were not rotating during transmission failure

## Slide 17
Case Study
Additional images of towing damage
Rear of Main Case/Rear Cover Removed
Rear Cover/P3 Planetary/P2 Carrier/Main Shaft

## Slide 18
Case Study
Additional images of towing damage
Main Shaft
P3 Carrier

## Slide 19
Case Study
Additional images of towing damage
Typical suction filter debris level due to starting vehicle in attempt to drive into shop