## Slide 1: Adaptation Components
Input adaptation components connect the transmission torque converter to the engine crankshaft.
  Front-end transmission component damage is often related to input adaptation.
  Visually inspect all adaptation components for wear, damage or distortion.
  Perform input adaptation measurements prior to installing the transmission.
Input Adaptation
Notes: <number>

## Slide 2: Adaptation Components (cont’d)
Input adaptation reference resources.
  The Mechanic’s Tips booklets.
  Service Information Letter (SIL) 60-TR-81 (available on the Allison Extranet).
Input Adaptation
Notes: <number>

## Slide 3: Measuring Tools
Required measuring tools:
  600mm (24 in.) vernier caliper
  50-100mm (2-4 in.) telescoping gauge
  25-76mm (1-3 in.) outside micrometer
  Dial indicator and mounting attachments
  0-150mm (0-6 in.) depth micrometer
Clean and inspect all components thoroughly prior to performing measurements.
When installing crankshaft bolts for measuring purposes, torque the bolts per the engine manufacturer’s recommendations.
Typical input adaptation measuring tools.
Input Adaptation
Notes: <number>

## Slide 4: Flywheel Housing Pilot Bore Diameter
Use an inside micrometer
or vernier caliper.
Measure the housing where the transmission torque converter
housing lip rests.
The measuring instrument should
intersect the housing centerline.
Input Adaptation
Notes: <number>

## Slide 5: Flywheel Housing Bore Runout
Mount the dial indicator base on the crankshaft hub.
Position the dial indicator button on the inside diameter of the flywheel housing.
Zero the dial indicator.
Rotate the crankshaft one complete revolution.
Read Total Indicated Runout (TIR) – all indicator movement both positive and negative.
Runout can sometimes be changed by repositioning the flywheel housing on the back of the engine.
Position the indicator on the housing inside diameter.
Input Adaptation
Notes: <number>

## Slide 6: Flywheel Housing Face Squareness
Mount the dial indicator base on the crankshaft hub.
Position the dial indicator button on the face of the flywheel housing.
Zero the dial indicator.
Rotate the crankshaft one complete revolution.
Read Total Indicated Runout (TIR).
Position the indicator button on the housing face.
Avoid allowing the button to contact bolt holes.
Input Adaptation
Notes: <number>

## Slide 7: Crankshaft Hub Pilot or Adapter Diameter
Measure using an inside micrometer or a telescoping gauge and outside micrometer.
Take measurements in at least two locations.
Place gauge in bore’s centerline.
Input Adaptation
Notes: <number>

## Slide 8: Crankshaft Hub Pilot or Adapter Face Squareness
Install the hub adapter if used – torque bolts to engine manufacturer’s specification.
Mount the dial indicator base on the flywheel housing.
Position the dial indicator button on the face of the hub pilot or adapter.
Zero the dial indicator.
Rotate the crankshaft one complete revolution.
Read Total Indicated Runout (TIR).
Torque crankshaft bolts to engine
manufacturer’s specification.
Input Adaptation
Notes: <number>

## Slide 9: Crankshaft Hub Pilot or Adapter Concentricity
Install the hub adapter if used – torque bolts to engine manufacturer’s specification.
Mount the dial indicator base on the flywheel housing.
Position the dial indicator button on the inside bore of the hub pilot or adapter.
Zero the dial indicator.
Rotate the crankshaft one complete revolution.
Read Total Indicated Runout (TIR).
Position the indicator button or
extension on the inside of the bore.
Input Adaptation
Notes: <number>

## Slide 10: Flexplate Bolt Hole Flatness
Install the hub adapter, flexplates, flexplate adapter and wear plate on the engine and torque the crankshaft bolts.
Mount the dial indicator base on the flywheel housing.
Position the dial indicator base on the flywheel housing.
Position the dial indicator button on the flexplates 292mm (11.5 in.) from the center of the crankshaft.
Zero the indicator.
Read Total Indicated Runout (TIR).
Avoid reading
crankshaft end play.
Input Adaptation
Notes: <number>

## Slide 11: Torque Converter Axial Location
1000 & 2000 Product Families
  Install the hub adapter, flexplates and wear plate and torque the bolts.
  Install the flexplate adapter to the flexplates and torque the bolts.
  Measure from the face of the flywheel housing to the face of the flexplate adapter 292mm (11.5 in.) from the center of the crankshaft.
Use a depth gauge to measure. Make sure
the crankshaft is thrust all the way rearward.
Input Adaptation
Notes: <number>

## Slide 12: Torque Converter Axial Location
3000 & 4000 Product Families
  Remove the flexplate adapter from the torque converter.
  Position the transmission output shaft down, torque converter installed.
  Use a depth gauge to measure from the face of the torque converter housing to the torque converter flexplate adapter mounting surface.
In this example, the straight-edge width is
subtracted from the depth gauge reading.
Input Adaptation
Notes: <number>

## Slide 13: Final Component Installation
Position the crankshaft hub adapter on the back of the engine.
Position the flexplates on the crankshaft hub adapter.
Position the wear plate on the installed flexplate.
Install and torque the bolts securing the entire assembly to the back of the engine.
Install the flexplate adapter to the flexplates or torque converter (depending on configuration) and torque the mounting bolts.
Typical adaptation hardware installation.
Input Adaptation
Notes: <number>