## Slide 1: Introduction
Perform a stall test to determine whether a power complaint is related to the engine or transmission.
Stall tests create high torque and high heat.
Do not stall test in Low or Reverse Range – use low torque ranges only.
Be aware of rapid transmission fluid temperature increase when stall testing.
Diagnostics –
Stall Test
Notes: <number>

## Slide 2: Stall Test Preparation
Install or use a known-good tachometer.
Install a temperature gauge in the transmission Converter-Out circuit.
Verify the transmission fluid level is correct at normal operating temperature (160-200 degrees Fahrenheit).
Verify that the engine throttle, air induction and smoke controls systems (if equipped) are operating properly.
Chock the vehicle wheels and clear all personnel from the front, sides and rear of the vehicle.
Turn off all vehicle accessories including the PTO.
Diagnostics –
Stall Test
Allison DOC™ can be used to monitor engine speed, transmission fluid temperature and to command a specific transmission range.
Notes: <number>

## Slide 3: Static Stall Test Procedures (Vehicle Stopped)
With the engine running, apply the parking brake and service brakes.
Shift the transmission into a forward range other than Low (if equipped).
Slowly depress the accelerator while holding the service brakes.
Record engine rpm when the tachometer stabilizes.
Slowly release the accelerator, select Neutral and cool the transmission by running the engine between 1200 and 1500 rpm.
Diagnostics –
Stall Test
Clutch Test
Notes: <number>

## Slide 4: Stall Testing Smoke Controlled Vehicles
Smoke controls and throttle delay mechanisms inhibit engine acceleration and may require stall testing with the vehicle moving.
  Locate an isolated area away from people and traffic.
  Select 2nd or 3rd range to limit road speed.
  Drive the vehicle at full throttle or maximum governed rpm.
  Slowly apply the service brakes while maintaining full throttle.
Diagnostics –
Stall Test
Notes: <number>

## Slide 5: Stall Testing Smoke Controlled Vehicles (cont’d)
Smoke controls and throttle delay mechanisms inhibit engine acceleration and may require stall testing with the vehicle moving.
  Record the engine rpm when vehicle comes to a complete stop.
  Release the throttle and allow the engine to return to idle.
  Select Neutral and run the engine between 1200 and 1500 rpm to cool the transmission.
Use Allison DOC™ to command and hold a specific range.
Diagnostics –
Stall Test
Notes: <number>

## Slide 6: Analyzing Stall Test Results
Reference the engine manufacturer’s stall test specification and compare to test results.
Diagnostics –
Stall Test
Stator
Turbine
Pump
Extremely Low Stall Speed
Engine Power Issue
Freewheeling Stator
Engine Power Issue
Slipping Clutches
Low Converter-Out Pressure
Stuck Stator
Cooling System Problem
Engine Power Issue
Low Stall Speed
High Stall Speed
Improper Cool Down
Result
Problem
Notes: <number>

## Slide 7: Analyzing Stall Test Results (cont’d)
Results often identify stator problems.
  Freewheeling stator symptoms:
    Extremely low stall speeds.
    No power at low vehicle speed but normal power at high vehicle speed.
    Elevated transmission fluid temperature.
    Transmission will not upshift under full throttle.
Diagnostics –
Stall Test
Stator
Turbine
Pump
Extremely Low Stall Speed
Engine Power Issue
Freewheeling Stator
Engine Power Issue
Slipping Clutches
Low Converter-Out Pressure
Stuck Stator
Cooling System Problem
Engine Power Issue
Low Stall Speed
High Stall Speed
Improper Cool Down
Result
Problem
Notes: <number>

## Slide 8: Analyzing Stall Test Results (cont’d)
Results often identify stator problems.
  Stuck stator symptoms:
    High torque converter-out temperature.
    Vehicle will not reach top speed.
    Transmission overheats at highway speeds.
Diagnostics –
Stall Test
Stator
Turbine
Pump
Extremely Low Stall Speed
Engine Power Issue
Freewheeling Stator
Engine Power Issue
Slipping Clutches
Low Converter-Out Pressure
Stuck Stator
Cooling System Problem
Engine Power Issue
Low Stall Speed
High Stall Speed
Improper Cool Down
Result
Problem
Notes: <number>