## Slide 1: Introduction
Proper driveline phasing and angularity minimize potential vibration and transmission damage.
Driveline measurements are entered into the Allison Installation Design Calculations software program for analysis.
Driveline Checks
Offset
Horizontal Slope
Vertical Slope and Length
Phasing
Notes: <number>

## Slide 2: Driveline Phasing
Yokes should typically be installed parallel to each other.
  Some vehicles are designed with yokes out of phase.
  Verify driveline design with OEM prior to changing phasing.
Phasing can be changed at the slip joint.
Driveline Checks
Typical slip joint
Notes: <number>

## Slide 3: Axle Vertical Slope
With the driveshaft removed, place an inclinometer against the axle.
Record the reading when the inclinometer stabilizes.
Driveline Checks
Notes: <number>

## Slide 4: Transmission Vertical Slope
Place an inclinometer on the bottom of the transmission.
Use a smooth, flat surface.
  Some transmission oil pans are not flat or parallel to the ground (including Allison 1000 & 2000 Product Families transmissions).
  On these models, place the inclinometer on the main housing where the oil pan mounts or place the inclinometer on the machined face of the output flange or yoke.
Record the reading when the inclinometer stabilizes.
Driveline Checks
Notes: <number>

## Slide 5: Axle & Transmission Horizontal Slope
Typically applies to V-drive transmissions which are not parallel to the frame rails.
In most applications a value of “0” is recorded for both measurements to indicate that the transmission and axle are parallel to the frame rail.
Driveline Checks
Notes: <number>

## Slide 6: Front and Rear Propshaft Slope
Place an inclinometer on the front and rear propshafts.
Use a smooth, flat surface.
  Record each reading when the inclinometer stabilizes.
Check each propshaft when the vehicle uses a multiple-piece driveline.
Driveline Checks
Notes: <number>

## Slide 7: Propshaft Length
Measure between the centers of each U-joint.
  Record each measurement.
Measure each propshaft when the vehicle uses a multiple-piece driveline.
Driveline Checks
Notes: <number>

## Slide 8: U-Joint Offset
Measure each propshaft’s position between the vehicle’s frame rails.
Tie a plumb bob to the frame rail and use it as a reference point.
Measure from plumb bob string to the center of each U-joint.
Record each measurement.
Driveline Checks
Notes: <number>

## Slide 9: Maximum Driveline Speed
Maximum driveline speed is maximum engine rpm divided by the highest transmission gear ratio.
Reference the engine data tag or engine manufacturer for max engine speed.
Driveline Checks
Notes: <number>

## Slide 10: Installation Design Calculations Software
Enter measurements and readings in the Allison Installation Design Calculations Software.
The software and support are available on the Allison Extranet.
Three key results must be within limits:
  Torsional Acceleration
  Drive U-Joint Inertial Acceleration
  Coast U-Joint Inertial Acceleration
The U-joint angles at each end of the driveline should be equal or nearly equal.
Driveline Checks
Notes: <number>