## Slide 1: Resources
A variety of preventive maintenance reference resources are available including:
  Mechanic’s Tips
  Operator’s Manual
  Service Information Letters (SILs), Service Tips and Tech Tips
  The Allison Transmission website
Reference these resources for:
  Procedures
  Recommended fluid and filter change intervals
  Recommended fluid types
  Refill capacities Product updates
Notes: <number>

## Slide 2: Inspection
Inspect the transmission, mounting components, the driveline and related vehicle systems during preventive maintenance.
  Check for loose mounting hardware and damaged components.
  Make sure wiring harnesses are properly secured, undamaged and connectors are in place.
  Make sure cooler lines or hoses are properly routed and secured; verify the lines and fittings are not leaking.
  Check for fluid leaks especially at seal and gasket areas.
Notes: <number>

## Slide 3: Drain Fluid & Filter Change
Drain the fluid.
  Warm the engine to normal operating temperature before draining the fluid.
  Remove the drain plug from the transmission oil pan.
  Examine the drained fluid for evidence of debris or contamination.
  Install and lube a new drain plug seal, then install and torque the drain plug.
Notes: <number>

## Slide 4: Drain Fluid & Filter Change (cont’d)
Remove the lube filter.
  Remove the cooler return filter assembly cover.
  Pull the filter from the housing.
  Remove the cover O-ring.
Notes: <number>

## Slide 5: Drain Fluid & Filter Change (cont’d)
Install the lube filter.
  Install and lube the cover O-ring.
  Lube the filter O-ring.
Install the filter, inserting it into the assembly and over the pilot inside the canister housing.
  Install and torque the cooler return filter assembly cover.
Notes: <number>

## Slide 6: Fluid Refill & Check
Refill the transmission with fluid.
  Reference the appropriate Allison publication for refill capacities and approved fluid types.
Start the engine, allow the fluid to warm, then check the level using the Oil Level Sensor.
  Add or drain fluid as needed.
Operate the vehicle, check for fluid leaks and re-check the fluid level.
Transmission fluid cools and lubricates the transmission and is critical to proper transmission operation and long transmission life.
Notes: <number>

## Slide 7: Resetting Prognostics Indicators
If enabled, prognostics must be reset after performing the fluid and filter change.
The Oil Life Monitor and Filter Life Monitor can be reset manually using the vehicle shift selector.
  Allison DOC® can also be used to reset prognostics.
Notes: <number>