## Slide 1: Introduction
SAE J1939 is a standard used for vehicle communication and diagnostics.
  Also called a “datalink” or a “Controller Area Network” (CAN).
  Faster and more reliable than previous J1708 and J1587 specifications.
J1939 reduces vehicle wiring and communicates a broad range of information including:
  Vehicle operation controls
  Powertrain interactions
  Vehicle management information
Reference the Allison Extranet for detailed datalink information including J1939.
Diagnostics –
J1939
1000/2000 Product Families J1939
Notes: <number>

## Slide 2: Cable Construction
SAE J1939-11 cable is shielded and includes a 120 ohm impedance twisted pair and a drain wire.
  Impedance affects the volume and rate of information flow and must be correct for proper databus operation.
  Mis-matched cables, tight bends, long breaks in shielding and improper cable design can affect impedance and performance.
  The proper wires, terminals, connectors and components must be used whenever building or repairing J1939 cables.
SAE J1939-15 (J1939 “Light”) uses unshielded cable and is not Allison recommended due to increased susceptibility to electromagnetic interference.
Diagnostics –
J1939
Notes: <number>

## Slide 3: Backbone Design
J1939 networks consist of a central “backbone” with “stubs” branching to individual controllers or “nodes.”
A 120 ohm termination resistor is required at each end of the backbone.
  Termination resistors can be built into some electronic components, including Allison 4th Generation Controls TCMs and J1939-based shift selectors.
Backbones may be no longer than 40 meters.
Stubs may be no longer than 1 meter and spaced at least 10 centimeters apart.
Diagnostics –
J1939
Notes: <number>

## Slide 4: Troubleshooting – Termination Resistors
With all controllers connected but powered off and both termination resistors in place, approximately 60 ohms resistance should exist between terminals A and B of a stub connector.
  Measure between terminals C and D on 9-pin in-cab diagnostic connectors.
120 ohms indicates one of the termination resistors is not installed.
  This can also indicate an open somewhere in the backbone.
0 ohms indicates a short between CAN high and CAN low wires.
  Short could be in the backbone or one of the stubs.
Diagnostics –
J1939
Notes: <number>

## Slide 5: Troubleshooting – Opens and Shorts
Opens can affect one or more controllers but will have the most impact on the controller attached to the affected stub.
Shorts typically generate multiple controller errors.
Opens and shorts can be located by performing continuity checks.
Diagnostics –
J1939
Notes: <number>

## Slide 6: Troubleshooting – Opens and Shorts (cont’d)
More advanced diagnostics can be performed using Allison DOC™.
  Use the Data Bus Viewer function.
  Reference Datalink Communications Tech Data for Parameter descriptions.
  Verify data is being broadcast and/or received.
Diagnostics –
J1939
Notes: <number>

## Slide 7: Troubleshooting – Inducted Noise
Proper backbone routing minimizes inducted noise issues.
Avoid routing near high-current switching devices:
  Solenoids
  Alternator
  Flasher modules
  High output CB radios
  Starter motors
  Relays
Use Allison DOC™ Data Bus Viewer to monitor datalink messages while trying to recreate the issue.
  Watch for errors or pauses in datalink traffic.
Diagnostics –
J1939
Notes: <number>

## Slide 8: Troubleshooting – Calibrations
Suspect an improper calibration or CMC settings if the system worked fine before, but not after recalibrating any networked controller software.
Potential Allison miscalibration causes:
  Auto-Detect completed before all controllers were connected to the datalink.
    Reset Auto-Detect using Allison DOC™
  The calibration was created with an incorrect datalink package, requiring installation of a new calibration.
Diagnostics –
J1939
TCM
CMC settings must be correct.
Notes: <number>

## Slide 9: Troubleshooting – Calibrations (cont’d)
Potential engine miscalibration causes:
  Transmission Type incorrectly set.
  Incompatible engine governor selected.
  Engine brake options incorrectly set.
  J1939 communication not activated.
Diagnostics –
J1939
TCM
CMC settings must be correct.
Notes: <number>